Top of Form

|  | Document ID# 1257363 2004 Saturn ION |  |
| --- | --- | --- |

Bottom of Form

Top of Form

Bottom of Form

# Engine Controls Connector End Views

| Table 1: | Crankshaft Position (CKP) Sensor |
| --- | --- |
| Table 2: | Engine Coolant Temperature (ECT) Sensor |
| Table 3: | Evaporative Emission (EVAP) Canister Purge Solenoid |
| Table 4: | Evaporative Emission (EVAP) Canister Vent Solenoid |
| Table 5: | Fuel Injector 1 |
| Table 6: | Fuel Injector 2 |
| Table 7: | Fuel Injector 3 |
| Table 8: | Fuel Injector 4 |
| Table 9: | Fuel Pump |
| Table 10: | Fuel Tank Pressure (FTP) Sensor |
| Table 11: | Heated Oxygen Sensor (HO2S) 1 |
| Table 12: | Heated Oxygen Sensor (HO2S) 2 |
| Table 13: | Idle Air Control (IAC) Valve |
| Table 14: | Ignition Control Module (ICM) |
| Table 15: | Intake Air Temperature (IAT) Sensor |
| Table 16: | Knock Sensor (KS) |
| Table 17: | Manifold Absolute Pressure (MAP) Sensor |
| Table 18: | Stop Lamp Switch-Lower (K34) |
| Table 19: | Stop Lamp Switch-Lower (w/o K34) |
| Table 20: | Throttle Position (TP) Sensor |

| Crankshaft Position (CKP) Sensor |
| --- |
| Connector Part Information | 15336024 2-Way F Metri-Pack 150 Series GT (BK) |
| Pin | Wire Color | Circuit No. | Function |
| 1 | PU | 574 | Low Reference |
| 2 | YE | 573 | CKP Sensor Signal |

| Engine Coolant Temperature (ECT) Sensor |
| --- |
| Connector Part Information | 15336024 2-Way F Metri-Pack 150 Series GT (BK) |
| Pin | Wire Color | Circuit No. | Function |
| 1 | BK | 2761 | Low Reference |
| 2 | YE | 410 | ECT Sensor Signal |

| Evaporative Emission (EVAP) Canister Purge Solenoid |
| --- |
| Connector Part Information | 12052643 2-Way F Metri-Pack 150 Series Sealed (RD) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 439 | Ignition 1 Voltage |
| B | D-GN/WH | 428 | EVAP Canister Purge Solenoid Control |

| Evaporative Emission (EVAP) Canister Vent Solenoid |
| --- |
| Connector Part Information | 12052643 2-Way F Metri-Pack 150 Series Sealed (RD) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 439 | Ignition 1 Voltage |
| B | WH | 1310 | EVAP Canister Vent Solenoid Control |

| Fuel Injector 1 |
| --- |
| Connector Part Information | 15326181 2-Way F (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 139 | Ignition 1 Voltage |
| B | BK | 1744 | Fuel Injector 1 Control |

| Fuel Injector 2 |
| --- |
| Connector Part Information | 15326181 2-Way F (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 139 | Ignition 1 Voltage |
| B | L-GN/BK | 1745 | Fuel Injector 2 Control |

| Fuel Injector 3 |
| --- |
| Connector Part Information | 15326181 2-Way F (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 139 | Ignition 1 Voltage |
| B | PK/BK | 1746 | Fuel Injector 3 Control |

| Fuel Injector 4 |
| --- |
| Connector Part Information | 15326181 2-Way F (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 139 | Ignition 1 Voltage |
| B | L-BU/BK | 844 | Fuel Injector 4 Control |

| Fuel Pump |
| --- |
| Connector Part Information | 776127-2 2-Way F AMP (BK) |
| Pin | Wire Color | Circuit No. | Function |
| 1 | PK/BK | 120 | Fuel Pump Supply Voltage |
| 2 | BK | 650 | Ground |

| Fuel Tank Pressure (FTP) Sensor |
| --- |
| Connector Part Information | 12059595 3-Way Metri-Pack 150 Series Sealed (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | RD/PK | 469 | Low Reference |
| B | GY/RD | 890 | Fuel Tank Pressure Sensor Signal |
| C | BN/WH | 416 | 5-Volt Reference |

| Heated Oxygen Sensor (HO2S) 1 |
| --- |
| Connector Part Information | 12160482 4-Way F Metri-Pack 150 Series Sealed (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | TN | 1667 | HO2S Low Signal Sensor 1 |
| B | PU | 1666 | HO2S High Signal Sensor 1 |
| C | D-GN | 676 | HO2S Heater Low Control Sensor 1 |
| D | PK | 439 | Ignition 1 Voltage |

| Heated Oxygen Sensor (HO2S) 2 |
| --- |
| Connector Part Information | 12160825 4-Way M Metri-Pack 150 Series (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | TN/WH | 1669 | HO2S Low Signal Sensor 2 |
| B | PU/WH | 1668 | HO2S High Signal Sensor 2 |
| C | BK/WH | 1423 | HO2S Heater Low Control Sensor 2 |
| D | PK | 439 | Ignition 1 Voltage |

| Idle Air Control (IAC) Valve |
| --- |
| Connector Part Information | 15354716 4-Way F GT 150 Sealed 3.2 X 4.0 (BLK) |
| Pin | Wire Color | Circuit No. | Function |
| A | L-GN/BK | 444 | IAC Coil B Low Control |
| B | L-GN/WH | 1749 | IAC Coil B High Control |
| C | L-BU/BK | 1748 | IAC Coil A Low Control |
| D | L-BU/WH | 1747 | IAC Coil A High Control |

| Ignition Control Module (ICM) |
| --- |
| Connector Part Information | 15329032 9-Way F (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 239 | Ignition 1 Voltage |
| B | WH | 423 | IC Timing Control |
| C-D | -- | -- | Not Used |
| E | BK/WH | 451 | Ground |
| F | BN/WH | 633 | CMP Sensor Signal |
| G | OG | 406 | IC Timing Control (B) |
| H-J | -- | -- | Not Used |

| Intake Air Temperature (IAT) Sensor |
| --- |
| Connector Part Information | 12162199 2-Way F Metri-Pack 150.2 Series Pull To Seat (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | TN | 472 | IAT Sensor Signal |
| B | BK | 2760 | Low Reference |

| Knock Sensor (KS) |
| --- |
| Connector Part Information | 12052643 2-Way F Metri-Pack 280 Series (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | D-BU | 496 | Knock Sensor Signal |
| B | GY | 1716 | Low Reference |

| Manifold Absolute Pressure (MAP) Sensor |
| --- |
| Connector Part Information | 12129946 3-Way F Metri-Pack 150 Series Sealed (M-GY) |
| Pin | Wire Color | Circuit No. | Function |
| A | OG/BK | 469 | Low Reference |
| B | L-GN | 432 | MAP Sensor Signal |
| C | GY | 2704 | 5-Volt Reference |

| Stop Lamp Switch-Lower (K34) |
| --- |
| Connector Part Information | 12041433 2-Way F Metri-Pack 280 Series (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 339 | Ignition 1 Voltage |
| B | PU | 420 | Stop Lamp Switch Signal |

| Stop Lamp Switch-Lower (w/o K34) |
| --- |
| Connector Part Information | 12033706 4-Way F Metri-Pack 280 Series (BU) |
| Pin | Wire Color | Circuit No. | Function |
| A | PK | 339 | Ignition 1 Voltage |
| B | PU | 420 | Stop Lamp Switch Signal |
| C-D | -- | -- | Not Used |

| Throttle Position (TP) Sensor |
| --- |
| Connector Part Information | 15326808 3-Way F GT 150 Sealed 4.5 (BK) |
| Pin | Wire Color | Circuit No. | Function |
| A | GY | 2701 | 5-Volt Reference |
| B | BK | 2752 | Low Reference |
| C | D-BU | 417 | TP Sensor Signal |

Top of Form

|  | Document ID# 1257363 2004 Saturn ION |  |
| --- | --- | --- |

Bottom of Form